## Slide 1
2 superconducting 3.8 km rings
2 large, 1 small experiments
100 GeV/nucleon Au
250 GeV polarized protons
Performance defined by
1. Luminosity L
2. Proton polarization P
3. Versatility (species, E)
Relativistic Heavy Ion Collider 1 of 2 ion colliders (other is LHC), only polarized p-p collider

## Slide 2: RHIC heavy ions – luminosity evolution to date
LNN = L N1N2 (= luminosity for beam of nucleons, not ions)
<L> = 15x design in 2011
About 2x increase in Lint/week each
Run-4 to Run-7
Run-7 to Run10
Run-10 to Run-11
Rate of progress will slow down – burn off 50% of beam in collisions already

## Slide 3: RHIC – effect of stochastic cooling in 2011
luminosity in 2 consecutive stores
with long. and vert. stochastic cooling
w/o cooling
w/o with cooling
Factor 2 gain in average luminosity from stochastic cooling so far – add horizontal cooling for Run-12
40ns
strong transverse cooling makes longitudinal cooling less efficient, i.e. these longitudinal profiles at the end of a store with be more pronounced with horizontal cooling next year
[hourglass factor 0.75 at beginning, 0.55 at end of store]
Notes: Stores: 16024 (prematurely ended by YA2 drop) and 16025, PHENIX luminosity, luminosity gain 16025/16024 = 1.9 (with 4.1h length both)
Cooling period shown: fillno 16002 to 16006 (Fri 06/03/11 and Sat 06/04/11)

## Slide 4: 56 MHz SRF for heavy ions – under construction (I. Ben-Zvi et al.)
l/4 Ni resonator
common to both beams
beam driven
56 MHz, 2 MV
Average luminosity vs. vertex size
Calculations Calculation by M. Blaskiewicz
40 ns
Longitudinal profile at end of store
even with cooling ions migrate into neighboring buckets
can be reduced with increased longitudinal focusing
demonstrated 2011 long. + ver. cooling
full 3D cooling
+ 56 MHz SRF
Commissioning planned for 2014
40ns
Notes: Longitudinal profile: 11676 Blue

## Slide 5: RHIC heavy ions – other luminosity limits
Operate close to a number of other limits:
Instabilities on ramp at transition (gtr = 26) driven by machine impedance and electron cloud
Beam loading during rf rebucketing limit removed last summer by separating common storage cavities
Intensity limit of beam dump (quench Q4) limit removed last summer by inserting sleeves in beam dump pipe
Bunch intensity limit from injector chain injected Nb = 1.5x109 in Run-11
Chromatic aberrations with small b* about 50% of particle loss due to burn-off, other 50% largely due to off-momentum dynamic aperture tested b* squeeze in store after cooling to equilibrium
at limit in 2007
at limit in 2010
at limit in 2010
at limit in 2011
Above list changes from year to year as most limiting effects are mitigated.

## Slide 6: Electron Beam Ion Source (EBIS) (J. Alessi et al.)
10 A electron beam creates desired charge state(s) in trap within 5 T superconducting solenoid
Accelerated through RFQ and linac, injected into AGS Booster
All ion species incl. noble gas, uranium and polarized 3He
Operated for NSRL with
He+, He2+, Ne5+, Ne8+, Ar11+, Ti18+, Fe20+
Commissioning for RHIC Run-12 under way
Work on ~2x Au32+ increase to design intensity (from transmission)
Received U cathode

## Slide 7: Au-Au energy scan to date
Peak and average luminosities fall faster than 1/g2 at lowest energies Need cooling at low energies to significantly increase luminosities

## Slide 8: e-cooling for low energy collider operation (A. Fedotov et al.)
Fermilab Pelletron (cooled 8 GeV pbar for Tevatron use) usable – scheduled for decommissioning in 3/2012, so far have not requested transfer
Cooling into space charge limit DQsc ~ 0.05 (new collider regime)
A. Fedotov et al. HB 2008
Expect up to factor 5 more integrated luminosity (depending on energy and DQsc)
with cooling
without cooling

## Slide 9: RHIC polarized protons – luminosity and polarization
At 250 GeV in 2011
Lavg = 90x1030cm-2s-1
Pavg = 48%
Lavg +60% rel. to 2009
Pavg +40% rel. to 2011
FOM = LP4 (longitudinally polarized beams)

## Slide 10: AnDY in 2011 (250 GeV pp)
Beam envelope function b* = 3.0 m at IP2
Reduced IP2 crossing angle from initially 2.0 mrad to zero
Added 3rd collision with following criteria:
      Nb ≤ 1.5x1011
      Beam loss rate <15%/h in both beams
      Not before first polarization measurement 3h into store
PHENIX
STAR
AnDY
small impact
visible impact,
few percent loss to STAR/PHENIX
loss rates
x/IP = 0.004
x/IP = 0.005
Notes: Criteria in effect from 8 April 2011, 22:08

## Slide 11: Optically Pumped Polarized H– source (OPPIS) – A. Zelenski
10x intensity increase was demonstrated in a pulsed operation by using a very high-brightness Fast Atomic Beam Source instead of the ECR source
Goals: 1. H− beam current increase to 10mA (order of magnitude) 2. Polarization to 85-90% (~5% increase)
Upgrade components:
1. Atomic hydrogen injector (collaboration with BINP Novosibirsk)
2. Superconducting solenoid (3 T)
3. Beam diagnostics and polarimetry
Upgraded OPPIS (2013)
Source Neutralizer Ionizer Rb-cell Sona Na-jet (H+) (H0) (H+) (H0) (H−)
sc solenoid
Superconducting solenoid delayed – may have impact on commissioning schedule.

## Slide 12: Electron lenses – partial head-on beam-beam compensation
Polarized proton luminosity limited by head-on beam-beam effect (DQbb,max ~ 0.02)
Basic idea: In addition to 2(3) beam-beam collisions with positively charged beam have another collision with a negatively charged beam with the same amplitude dependence.
-- Electron lenses are used in the Tevatron --
Exact compensation for:
short bunches
Dyx,y = kp between p-p and p-e collision
no nonlinearities between p-p and p-e
same amplitude dependent kick from p-p, p-e
only approximate realization possible
Expect up to 2x more luminosity with OPPIS upgrade Commissioning planned for 2013
e-gun
e-collector
main solenoid manufacturing in SMD
GS1 manufacturing in industry

## Slide 13: Polarized 3He – Workshop 28-30 September 2011
Developing plan for implementation
3Heh source being developed with MIT
3Heh in EBIS/Booster/AGS
3Heh in RHIC may require 6 snakes in 1 ring
Polarimetry
Implementation technically possible in ~3-4 years

## Slide 14: High-luminosity polarized proton operation
Will probably not exceed Lpeak~1033cm-2s-1 at √s = 500 GeV without cooling, or superbunches (say 6 bunches filling ½ circumference)
Coherent Electron Cooling PoP test in preparation (V. Litvinenko et al)
Collision scheme with crossing angle and cooling could boost luminosity by another factor ~5

## Slide 15: RHIC luminosity and polarization goals
parameter |  | unit | achieved |  | goals |  |  | 
Au-Au operation |  |  | 2011 |  | ≥ 2014 3D stochastic cooling + 56 MHz SRF |  |  | 
energy | GeV/nucleon |  | 100 |  | 100 |  |  | 
no colliding bunches | … |  | 111 |  | 111 |  |  | 
bunch intensity | 109 |  | 1.3 |  | ≥ 1.1 |  |  | 
avg. luminosity | 1026 cm-2s-1 |  | 30 |  | 40 |  |  | 
p-p operation |  |  | 2009 / 2011 |  | ≥ 2012 |  | ≥ 2014 source + e-lenses | 
energy | GeV |  | 100 | 250 | 100 | 250 | 100 | 250
no colliding bunches | … |  | – 107 – |  | – 107 – |  | – 107 – | 
bunch intensity | 1011 |  | 1.3 | 1.65 | 1.3 | 1.7 | 1.7 | 2.5
avg. luminosity | 1030 cm-2s-1 |  | 24 | 90 | 30 | 150 | 60 | 300
avg. polarization* | % |  | 56 | 48 | – 60 – |  | – 70 – | 
*Intensity and time-averaged polarization as measured by the H-jet. Luminosity-averaged polarizations, relevant in single-spin colliding beam experiments, are higher. For example, for intensity-averaged P = 48% and Rx = Ry = 0.2 (250 GeV, 2011), the luminosity-averaged polarization is P = 52%.

## Slide 16
http://www.rhichome.bnl.gov/RHIC/Runs/

## Slide 17
eSTAR
ePHENIX
eRHIC Design
2 SRF linac
1 -> 5 GeV per pass
4 (6) passes
Vertically separated
recirculating passes.
# of passes will be chosen
to optimize eRHIC cost
Coherent
e-cooler
5 mm
5 mm
5 mm
5 mm
20 GeV
e-beam
15 GeV
e-beam
10 GeV
e-beam
5 GeV
e-beam
Common vacuum chamber
Gap 5 mm total
0.3 T for 30 GeV
eRHIC detector
injector
RHIC: 250 GeV p or 100 GeV/u Au with DX magnets removed
eRHIC-I & eRHIC: energy of electron beam is increased from 5 GeV to 30 GeV by building up the linacs
Design allows for:
multiple IP’s
reusing infra-structure + det. components for STAR, PHENIX?
easy up-grade
IR design to reach 1034cm-2s-2 luminosity