## Slide 1: RHIC Status: Startup Run 12
V. Schoefer
RHIC Spin Collaboration Meeting
1/13/12

## Slide 2: Outline
Startup schedule
Improvements for Run 12
  Further LLRF commissioning
  9 MHz
  Luminosity
    Slight reduction in beta* (100 GeV)
    Emittance measurement, reduction and maintenance
  Polarization
    Source improvements (Einzel lens + suppression tune)
    Store energy change (250 GeV polarization lifetime)
    Emittance improvements
    Possible ramp transmission improvements (100->250 GeV)
Lattices and projection

## Slide 3: Start Up Outline
Jan 3-9: Successful, addressing outstanding items now
Jan 17 : Start of final cooldown
Jan 21: Earliest injection into blue
  Followed by 9 MHz capture
  Instrumentation setup
Jan 24: Yellow injection
  Followed by 9 MHz capture
  Instrumentation setup
Sat Jan 28: Power supplies ready for ramp
  Actual readiness for ramp depends on LLRF progress
  Beam-to-flattop time expected to be short (~ 1 ramp)
by Friday Feb 3: Midnight shift collisions (day/eve still development)
week of Feb 6: Final ramp up and into production with 100 GeV

## Slide 4: RF: Low-level
Addresses problems from last year: reliability, emittance growth
  9 Mhz bouncer feedback loops improved for less noise
  ‘bunch-gating’: will allow bunch-to-bucket phase feedback during injection, preserves emittance while sitting at injection
Independent control of AGS extraction energy for extraction to blue/yellow
  9 MHz matching very sensitive to energy error
I expect this to be the pacing item for startup

## Slide 5
RF: High level - 9 MHz Cavity
Burned up spring fingers
Loose linkage in tuning servo
Two source of downtime in Run 11:
  Mechanical linkage in the tuning servo of the 9 MHz cavity was loose. This was very hard to trouble shoot
  High-level rf failure (spring fingers)
Loose linkage slowed the startup/ramp
Burned RF spring fingers caused the version to 28 MHz ramps in the last week of the run
Both issues resolved. RF shield redesigned to eliminate hot spot
We will start Run 12 with the 9MHz cavity
Rebucketing to 28 MHz at store and squeeze with 197 MHz

## Slide 6: Emittance Monitoring
Vertical emittance in AGS is difficult to measure/maintain (near integer)
New dipole installed to measure the (rapidly changing) optics immediately at the IPM through the cycle
  Can better quantify growth at injection
  Maybe can identify growth on the ramp
Similar method available for optics measurement in RHIC
New flags installed in AtR for precision measurement of transfer optics
  Addresses discrepancy between blue and yellow transmission and possible emittance dilution at RHIC injection

## Slide 7: Emittance: Consistency
If the Run 11 ZDC calculated emittances were capped at their MEDIAN value, that is a 10 % decrease in average emittance.
20 % increase in luminosity, just from consistently meeting a relatively weak constraint.
More precise measurement and monitoring will help
(from lumi)

## Slide 8: Polarization Transmission in RHIC
Acceleration of beam from
100 GeV to 250 GeV and back to 100 GeV suggests 10 % (absolute) polarization loss between 100 and 250 GeV.
The mechanism for the remaining loss is not well-understood and continues to be studied with tracking.
Not a clear step down at the location of an identifiable resonance

## Slide 9: Possible RHIC Polarization Loss Mechanisms
Sub-optimal store energy: polarization lifetime (loss of 5%, absolute, during 250 GeV store)
Transverse coupling during the ramp
  Global coupling appears well-corrected
  Fast local coupling measurement for Run 12
10 Hz orbit oscillations
  Feedback on the ramp demonstrated with Au in Run 11
Vertical dispersion
  Primary source is our own coupling correction, new correction algorithm to be tested in Run 12

## Slide 10: Ramp coupling
Betatron frequency
Horizontal
Vertical
Blue
Yellow
100 250 100
100 250 100
GeV
GeV

## Slide 11: Orbit oscillations at 10 Hz
Vertical position (um)
Time since ramp start (s)
Mechanical vibration of triplet quads causes transverse position oscillations. Horizontal change is of order 2-3 mm, but 200 um (peak-to-peak) in vertical
--- Feedback off
--- Feedback on
Feedback routinely used at store through Run 11, demonstrated effective on the ramp only at the end of Run 11 during the heavy ion run.

## Slide 12: RHIC 100 GeV Polarized Proton Parameters
Parameters | Run 12 Goal
Interaction points | 6 8
* in blue [m] | 0.85 0.85
* in yellow [m] | 0.85 0.85
Working points (ramp and store) | 28.695, 29.685
Luminosity/Week | 10 pb-1 (max)
Polarization (Jet) | 60-65%
Peak bunch intensity | 1.35  1011
Peak luminosity | 0.5  1032 cm-2s-1
No tune swing
Down from 1 m in Run 9

## Slide 13: RHIC 250 GeV Polarized Proton Parameters
Parameters | Run 11 Achieved | Run 12 Goal
Interaction points | 6 8 (AnDY test at 2) | 6 8
* in blue [m] | 0.8 0.6 | 0.65 0.65
* in yellow [m] | 0.65 0.63 | 0.65 0.65
Working points | Ramp: (28.680, 29.673) Store: (28.69, 29.68) | Ramp: (28.680, 29.673) Store: (28.69, 29.68)
Luminosity/Week | 25.4 pb-1 (the best, 4/5-12) | 40 pb-1 (max)
Polarization (Jet) | 46%* | ~50%
Peak bunch intensity | 1.65  1011 | 1.65  1011
Peak luminosity | 1.6  1032 cm-2s-1 | 2.0  1032 cm-2s-1
*Average of jet polarization is 46% for both rings. Taking into account for the polarization profile correction factor (R=0.2), The polarization seen by experimenters is boosted by Sqrt(1+R)=> 50%.
Notes: Peak luminosity goal nearly achieved, but at higher intensity than anticipated.
Higher intensity is a product of the 9 MHz cavity commissioning.
Problem is the emittance.