## Slide 1: Polarized proton projections Wolfram Fischer
11 May 2012
RHIC Spin Collaboration Meeting BNL
Notes: 9 August 2011, 14:30, 25+5min

## Slide 2: Run-12 100 GeV polarized protons
Polarization (H-jet, i.e. intensity and time averaged)
Blue 56g61.8% Yellow 57g56.6% (2009g2012)

## Slide 3: Run-12 255 GeV polarized protons
Polarization (H-jet, i.e. intensity and time averaged)
Blue 48g50.3% Yellow 48g53.5% (2011g2012)

## Slide 4: RHIC time-in-store
Low failure rates of all systems, even at raised energy.

## Slide 5: RHIC polarized protons – luminosity and polarization
At 255 GeV in 2012
Lavg = 105x1030cm-2s-1
Pavg = 52%
Lavg +15% relative to 2011
Pavg +8% relative to 2011
FOM = LP2 (single spin experiments)
FOM = LP4 (double spin experiments)

## Slide 6: New in Run-12 Run Coordinator: V. Schoeffer
100 GeV
2 new Landau cavities installed
Yellow primary collimator inspected (no sign of damage – concern for high intensity)
AGS horizontal alignment
9 MHz system upgraded
AGS horizontal tune jump system timing improved
Operation from new MCR
Down ramps do not stop at park, park to injection 2x faster
255 GeV
Increased store energy
Snake ramps between 100 GeV and 255 GeV
Scans of snake spin rotation axis angle and rotation angle
Test of longitudinal injection damper, Landau phase error compensation
Test of short AGS cycle
Test of Blue vertical phase shifter power supply (for electron lenses)

## Slide 7: Polarization in Run-12
Difference between Blue and Yellow not understood (100 GeV PB > PY, 255 GeV PB < PY)
Expect only small further gains in ramp transmission
Polarization lifetime at store cannot be easily eliminated
Further P gains likely to come from source upgrade: larger initial polarization, and ability to reduce emittance

## Slide 8: Preparation for Run-13 pp
OPPIS upgrade
Electron lens installation
  Also requires a new lattice (phase advance between IP8 and IP10 – phase shifters)
Polarimeter improvement
  RF properties of pC polarimeter
  Targets
RF
  9 MHz modification
  Longitudinal injection damping
  Landau phase compensation

## Slide 9: Optically Pumped Polarized H– source (OPPIS) – A. Zelenski
10x intensity increase was demonstrated in a pulsed operation by using a very high-brightness Fast Atomic Beam Source instead of the ECR source
Goals: 1. H− beam current increase to 10mA (order of magnitude) 2. Polarization to 85-90% (~5% increase)
Upgrade components:
1. Atomic hydrogen injector (collaboration with BINP Novosibirsk)
2. Superconducting solenoid (3 T)
3. Beam diagnostics and polarimetry
Upgraded OPPIS (2013)
Source Neutralizer Ionizer Rb-cell Sona Na-jet (H+) (H0) (H+) (H0) (H−)
sc solenoid

## Slide 10: OPPIS location 05/10/12
New Atomic Beam Source (ABS)
New superconducting solenoid

## Slide 11: RHIC electron lenses Motivation
Bunch intensity in 2012 polarized proton physics store
bunches with 1 collision
bunches with 2 collisions
Goal:
Compensate for 1 of 2 beam-beam interactions with electron lenses
Then increase bunch intensity and luminosity (up to 2×)
Need with new polarized proton source − under construction, A. Zelenski

## Slide 12: RHIC electron lenses Compensation overview
Basic idea: In addition to 2 beam-beam collisions with positively charged beam have another collision with a negatively charged beam with the same amplitude dependence – and electron lens.
Exact compensation for:
short bunches
Dyx,y = kp between p-p and p-e collision
no nonlinearities between p-p and p-e
same amplitude dependent kick from p-p, p-e
only approximate realization possible
Deviations from ideal were extensively studied in simulations: Y. Luo et al. – accepted for publication PRST-AB
Build on experience with Tevatron electron lenses V. Shiltsev, A. Burov, A. Valishev, G. Stancari, X.-L. Zhang, …
BNL Electron Beam Ion Source (EBIS) J. Alessi, E. Beebe, M. Okamura, A. Pikin, D. Raparia, …
FNAL - TEL
BNL - EBIS

## Slide 13: RHIC electron lenses Compensation overview
p
p
Electron gun Modes: DC, 100 Hz (setup), 80 kHz (1/turn)
Vmax = 10 kV, Imax = 1.5 A, P = 2×10-6 AV-3/2… Cathodes: LaB6 and IrCe (from Budker), 4.1 mm radius, Gaussian profile (2.8 s)
GS1 warm solenoid B = 0.8 T, I = 1200 A, P = 58 kW
GS2 warm solenoid B = 0.5 T, I = 730 A, P = 25 kW
GSB warm solenoid B = 0.3 T, I = 770 A, P = 45 kW
Electron collector rP < 50 W/cm2, T < 125 °C
CSB = GSB
CS2 = GS2
CS1 = GS1
SC main solenoid B = 6 T, I = 440 A + 16 more magnets
GSX/Y
CSX/Y = GSX/Y

## Slide 14: Electron lenses some hardware

## Slide 15: Luminosity and Polarization Goals
Parameter | unit | Achieved | With 3D stoch. cooling and 56 MHz SRF | 
Au-Au operation |  | 2011 | ≥ 2014 | 
Energy | GeV/nucleon | 100 | 100 | 
No of bunches | … | 111 | 111 | 
Bunch intensity | 109 | 1.3 | 1.1 | 
Average Luminosity | 1026 cm-2 s-1 | 30 | 40 | 
p- p operation |  | 2012 | ≥ 2013 | ≥ 2014
Energy | GeV | 100 / 255 | 100 / 250 | 250
No of bunches | … | 109 | 109 | 109
Bunch intensity | 1011 | 1.6 / 1.7 | 1.6 / 2.0 | 2.2
Average Luminosity | 1030 cm-2 s-1 | 33 / 105 | 30 / 150 | 300
Polarization | % | 58 / 52 | 60 | 70

## Slide 16: Luminosity projections for Run-13
Polarization: 50-60% (depends largely on OPPIS progress)
Luminosity: electron lens commissioning, expect limited gains

## Slide 17: Projections for p⌃-p⌃
incremental changes (ex,y, es, DEstore, db/b…)
polarized source upgrade electron lens commissioning
incremental changes
[Note: assume 12 weeks of physics, 8 weeks of ramp-up, start at ¼ of max]

## Slide 18: Polarized proton projections – summary
Have transformed Run-11 developments into operation in Run-12
Polarization
  Further gains likely require source upgrade
  Difference between Blue and Yellow not yet understood (both 100 GeV and 255 GeV)
Upgrades
  OPPIS (expect gains in polarization and/or luminosity in Run-13)
  Electron lenses (commissioning in Run-13, expect limited gains)
  Longitudinal emittance
  Polarimetry