## Slide 1: Hydrogen Jet Polarimeter Results from Run6
Kieran Boyle
(Stony Brook University)

## Slide 2: Outline
HJet Status in Run6
Analysis Cuts
100 GeV
  Asymmetries & Polarizations
    Method
    Results
      Overall
      Fill by Fill
  Systematics
    Bunch Shuffling
    Background Contribution
31 GeV
  Blue Beam Asymmetries & Polarization
    Results
    Systematics
  Yellow Beam Status

## Slide 3: How to get elastic protons
Using non-relativistic kinematics, we have
TR = Recoil energy
R = recoil angle
mp = mass of proton
So ToF and TR are related giving us a “banana” plot
Elastically scattered protons will have and TR-R correlation, i.e. TR-strip correlation.
TR (MeV)
ToF (ns)
ToF (ns)
TR (MeV)

## Slide 4: HJet Status During Run6
Always ran with only one beam on target.
  Second Beam was displaced vertically and horizontally.
1 pad (detector) out of six died on April 10
  No energy calibration for this sensor in Run6, so excluded from the analysis
x

## Slide 5: Yields (Banana plots): Blue
Banana cut of 2 applied around proton peak
TR (MeV)
ToF (ns)

## Slide 6: Yield per strip (Blue beam)
Define signal region based on two strips with maximum yield
Use two strips to reduce background contibution
strip number
1
2
3
4
5
6

## Slide 7: Asymmetry
Use simple square root formula
Measure two different asymmetries
  target:Target polarized, beam unpolarized
  beam: Target unpolarized, beam polarized
Ratio between two asymmetries, scaled by target polarization, gives beam polarization:
Ptarget = 92.4% +/- 1.8%


## Slide 8: Valid Energy Range
For result, use only 1-4 MeV protons
Above 4 GeV, protons may punch through detector, and so reconstructed energy is incorrect.
Below 1 GeV, ToF calibration is not reliable, as particle path is affected by magnetic holding field.


## Slide 9: 100 GeV

## Slide 10: Results (Run 6 100 GeV)
From the whole running period.
ON LEFT:
  Asymmetries for Yellow (top) and Blue (bottom) running periods
ON RIGHT
  Ratio of beam asymmetries for Yellow (top) and Blue (bottom) beams.
  Result only uses data from 1-4 MeV
Blue
Yellow
target (Y)
beam (Y)
target (B)
beam (B)

## Slide 11: Final Jet Results (100 GeV)
Results based on combined statistics from 1-4 MeV.
stat

## Slide 12: Polarization Fill By Fill (100 GeV)
Results from fill by fill analysis using combined statistics from 1-4 MeV.
PB

## Slide 13: Asymmetries By Fill
Fill By Fill asymmetries.
target is stable. Fluctuation is in beam.

## Slide 14: Comparison with Run 5
To ensure that jet is consistent between years, we can compare target asymmetries.
Target asymmetries should be constant as Target polarization is 92.4% +/- 1.8% for both years.
Results are in good comparison.
Run6 Blue
Run6 Yellow
Run5 Blue
Run5 Yellow
target
beam

## Slide 15: Background Corrected target
Correct target for background assuming background is asymmetry free.

## Slide 16: Final Jet Results (100 GeV)
Results based on combined statistics from 1-4 MeV.
stat

## Slide 17: Systematic Uncertainty

## Slide 18: Bunch Shuffling: Yellow
Randomize spin pattern, while retaining bunch yield information.
Plot Ashuf/Ashuf
Deviation from =1 in Gaussian shows level of systematics
Results show slight deviation from 1, less than Run5
1.0<TR<1.5
1.5<TR<2.0
2.0<TR<2.5
2.5<TR<3.0
3.0<TR<3.5
3.5<TR<4.0
Ashuf/Ashuf

## Slide 19: Bunch Shuffling: Blue
Randomize spin pattern, while retaining bunch yield information.
Plot Ashuf/Ashuf
Deviation from =1 in Gaussian shows level of systematics
Results show slight deviation from 1, less than Run5
Ashuf/Ashuf
1.0<TR<1.5
1.5<TR<2.0
2.0<TR<2.5
2.5<TR<3.0
3.0<TR<3.5
3.5<TR<4.0

## Slide 20: Background effect
Three main sources of background:
  Elastic Scattering from Molecular Hydrogen
    If we assume unpolarized, then beam and target asymmetries differ. Accounted for in polarization of target. (96%  92.4%)
  Non-elastic Scattering
    Forward for target, backward for beam so can be different. Estimate possible asymmetry.
  Elastic Scattering from other beam
    Dilutes both beam and target
      When considering one beam, other is spin averaged
      Scattering from target to our acceptance (light green) is backward scattering from target (or forward scattering from unpolarized H2)—so no spin dependence.

## Slide 21: How to Study Non-Elastic
Use two peak strip for signal (red).
Use strips closer to perpendicular for BG1 (purple).
Use strips farther from perpendicular for BG2 (green).
  Note that there is no acceptance above 2 MeV.
Leave 1 strip between peak and BG out.

## Slide 22: Results for different regions
Use BG2 to estimate size of possible asymmetry in non-elastic collisions
Based on this asymmetry, and background contribution, estimate possible effect on polarization
Beam polarization will scale with this effect
Systematic uncertainty
BG1
BG2
signal
target (Y)
beam (Y)
target (B)
beam (B)

## Slide 23: Summary of systematic uncertainty at 100 GeV
Target Polarization: PTsys = 1.8%
  accounts for molecular hydrogen component
Non-elastic Background:
  Yellow: PINsys = 1.5%
  Blue: PINsys = 1.3%
Other beam Background:
  Dilutes both asymmetries. Analytic calculations shows effect on polarization is <10-4.

## Slide 24: 31 GeV

## Slide 25: Analysis
Similar to 100 GeV
Cuts are the same

## Slide 26: Background in Blue
Backgrounds in blue similar to 100 GeV
Shaded green are signal strips.
0.5<TR<1.0
1.0<TR<1.5
1.5<TR<2.0
2.0<TR<2.5
2.5<TR<3.0
3.0<TR<3.5
3.5<TR<4.0
4.0<TR<6.0
Strip

## Slide 27: 31 GeV Blue Asymmetry
Background in blue beam is reasonable
Final Blue beam polarization:
  P = 0.469
  Pstat = 0.019
target (Y)
beam (Y)
target (B)
beam (B)

## Slide 28: Background Problem in Yellow
Backgrounds much larger in Yellow beam.
Reason is not entirely clear.
How does this affect beam polarization measurement
Strip
0.5<TR<1.0
1.0<TR<1.5
1.5<TR<2.0
2.0<TR<2.5
2.5<TR<3.0
3.0<TR<3.5
3.5<TR<4.0
4.0<TR<6.0

## Slide 29: 31 GeV Yellow Asymmetry
Yellow beam has large background which clearly affects measured asymmetry of target.
May imply that effective target polarization is different from 92.4%
Therefore extraction of beam polarization is unreliable
target (Y)
beam (Y)
target (B)
beam (B)

## Slide 30: Compare Asymmetries
Blue and yellow beam asymmetries are similar
Target asymmetries are quite different, due to background.
As Yellow target asymmetry is unreliable at 31 GeV, we must use Blue beam to normalize.
Sasha will discuss additional uncertainty due to this more, but is ~2.2 3%
target (Y)
beam (Y)
target (B)
beam (B)

## Slide 31: Study Non-Elastic at 31 GeV
Method same as at 100 GeV:
  Use two peak strip for signal (red).
  Use strips closer to perpendicular for BG1 (purple).
  Use strips farther from perpendicular for BG2 (green).
    Note that there is no acceptance above 2 MeV.
  Leave 1 strip between peak and BG out.

## Slide 32: Results for different regions: 31 GeV
Use BG2 to estimate size of possible asymmetry in non-elastic collisions
Based on this asymmetry, and background contribution, estimate possible effect on polarization
Beam polarization will scale with this effect
Systematic uncertainty
BG1
BG2
signal
target (Y)
beam (Y)
target (B)
beam (B)

## Slide 33: Summary of systematic uncertainty at 31 GeV for BLUE beam ONLY
Target Polarization: PTsys = 1.8%
  accounts for molecular hydrogen component
Non-elastic Background:
  Blue: PINsys = 1.9%
Other beam Background:
  Dilutes both asymmetries. Analytic calculations shows effect on polarization is <10-4.

## Slide 34: Summary
Final Results at 100 GeV are presented.
  Will be used for normalizing pC
  Result for target asymmetry consistent with Run5
  Systematic Uncertainty similar to Run5
Final Result at 31 GeV are presented
  Blue beam has low background, and will be used to normalize blue beam
  Yellow beam has high backgroundbeam polarization from Jet not reliable.
    Use blue beam to normalize yellow pC
    Sasha will discuss uncertainty due to this

## Slide 35: Backups

## Slide 36: Get Data
Get ADC and TDC of data.
Floating trigger timing, so must acount for when trigger occurs.
Subtract of baseline from max ADC.
Calculate TDC at ADC(TDC)=½ADCmax
TDC½
baseline
ADCmax

## Slide 37: Calibrations

## Slide 38: Energy Calibration: Data
Calibration Runs for Run6
  1904.401 4/19
  0506.403 6/05 (End of 200 GeV running)
  0612.402 12/06 (six months after run)
Again, for all calibration runs, detector 5 is not working at all. Detector 5 died ~ Apr. 10
Run5 calibrations are different from Run6, and so cannot be used for data before April 10.

## Slide 39: Energy Calibration: Method
Use the same method as for Run5
So, as we have 4 possible peaks, for each channel we have at most 4 equations

## Slide 40: Energy Calibration: Results
From ADC distribution, extract peak value.
3 detectors have Gd and Am source (includes dead detector), 3 have only Am.
Two peak structure due to different entrance window thicknesses
Using method described in the Run5 analysis note, we get energy calibration constants.
Calibration Constants (MeV)
dead
detector
Gd
Am
from 4/19

## Slide 41: ToF Calibration: Method
Main idea: Compare measured ToF (TDC*2.38 ns) with expected ToF from a proton with the measured energy assuming non relativistic kinematics
So plot histogram of ToFcalc – ToFmeas, and then extract calibration constant.
Reality is one step more complicated

## Slide 42: ToF Calibration: Step 1
1
2
Not so good
TR
ToFmeas
ToFmeas
ToFmeas - ToFcalc

## Slide 43: ToF Calibration: Step 2
1
2
Not so good
Better
3
4

## Slide 44: ToF Calibration: Results
Blue dots are for yellow beam on target.
  Ignore red dots which are the other beam, and not well calibrated.
From left to right are the 6 detectors (1 is dead).
Drop at left is in very low energy protons, which have problems due to energy loss at the entrance window of silicon, and due to magnetic field affecting traveled path.

## Slide 45: Yield per strip (Yellow beam, 100 GeV)
Define signal region based on two strips with maximum yield
Use two strips to reduce background contibution

## Slide 46: Sys. Error due to Background
For result, we use two strips correlated with energy.
Dilution factor due to molecular hydrogen component reduces target polarization (main background source) from 96% to 92.4%.
However, this assumes molecular hydrogen component is not polarized. If background is polarized, directly affect measurement.
Estimate systematic uncertainty in polarization by varying amount of background (i.e use fewer or more strips).
Results show increase in ratio as more background is included.

## Slide 47: Results From Run5
Not planning on showing this Friday, but just for comparison.
Oleg used maximum difference as systematic error (1.1%/PB)
For Run6, this would give 1.8%/PB
1.1%

## Slide 48: Hint that inelastic effect is 0?
…at 31 GeV anyway.
Backgrounds are very different.
When correct both results for backgrounds assuming 0 asymmetry in background, results agree within stat.
Yellow
Blue