## Slide 1: The STAR FGT upgrade program
Xuan Li for the STAR Collaboration
Temple University
STAR

## Slide 2: Outline
Motivation
  Forward GEM Tracker (FGT) physics program
FGT overview
  Assembly and installation
  Cosmic ray results for RHIC Run 13
FGT upgrade and open discussion for p+A collisions
Summary

## Slide 3: Motivation
Other channels?
How about polarized sea quark distribution?
T.C.Awes et al.,
Phys.Rev.D58:092004,1998
Asymmetry of unpolarized sea quark distribution function had been found in Drell-Yan process (p+N μ+μ-).

## Slide 4: W production – unique new probe to measure quark polarization
Probing polarized quark distribution via W production.

## Slide 5: W measurement at STAR
STAR AL results and projection.

## Slide 6: W measurement at STAR
Measured asymmetries (Run 9) are in agreement with theory evaluations using polarized pdf’s (DSSV) constrained by polarized DIS data
⇒ Universality of helicity distr. functions!
STAR AL results and projection.

## Slide 7: W measurement at STAR
Measured asymmetries (Run 9) are in agreement with theory evaluations using polarized pdf’s (DSSV) constrained by polarized DIS data
⇒ Universality of helicity distr. functions!
STAR AL results and projection.
Critical: Measurement of W+ and W- asymmetries as a function ηe

## Slide 8: W measurement at STAR
Measured asymmetries (Run 9) are in agreement with theory evaluations using polarized pdf’s (DSSV) constrained by polarized DIS data
⇒ Universality of helicity distr. functions!
STAR AL results and projection.
Critical: Measurement of W+ and W- asymmetries as a function ηe
Extension of backward / forward ηe acceptance enhances sensitivity to anti-u / anti-d quark polarization
⇒ STAR Forward GEM Tracker (1<|ηe|<2)

## Slide 9: W measurement at STAR
Measured asymmetries (Run 9) are in agreement with theory evaluations using polarized pdf’s (DSSV) constrained by polarized DIS data
⇒ Universality of helicity distr. functions!
STAR AL results and projection.
Critical: Measurement of W+ and W- asymmetries as a function ηe
Extension of backward / forward ηe acceptance enhances sensitivity to anti-u / anti-d quark polarization
⇒ STAR Forward GEM Tracker (1<|ηe|<2)

## Slide 10: GEM technology
Gas Electron Multiplier technology used for its high resolution capabilities at a very low mass.
GEMs use a high electric field in the holes of a copper coated foil to amplify very small signals produced by ionizing particles.
Hole diameter:
Pitch:
Single GEM
in electic field
Ionizing particles pass through Triple GEM

## Slide 11: FGT overview - design
Design constraints
  Low mass which is important being close to interaction region.
  Size limited by GEM foil production technology.
  High rate – around 0.5MHz/cm2, very radiation tolerant.
FGT installed inside STAR

## Slide 12: FGT overview - construction
Forward GEM Tracker - layout
Quarter section
Disk
FGT consists of 6 disks
West Support Cylinder (WSC)
for FGT
The FGT has been
fully installed in STAR
for RHIC Run 13.

## Slide 13: Look inside FGT quadrant
FGT quarter section - layout
Read out R, φ
value to determine
hit position
Read out R
Read out φ
Short Octant
Long Octant

## Slide 14: Look inside FGT quadrant
FGT quarter section - layout
HV layer
2D readout board
Readout module
APV chip
HV board
Interconnect board
Pressure volume
Pressure volume

## Slide 15: FGT installation and calibration
FGT has been fully installed in STAR for RHIC run13.
Tune HV and APV parameters with three layers of FGT quadrants in cosmic ray test.
Trigger scintillating counters not shown in this picture located above and below the FGT cosmic ray setup.

## Slide 16: FGT cosmic ray – Gain curve
Gain VS HV
3.3kV
3.4kV
3.5kV
Cluster threshold = 4*PedRMS(~40)*3timebin ~ 500
ADC saturate at peak time-bin of peak strip for
~10% of pulses at 3.4kV
~50% of pulses at 3.5kV (but no visible effect on residual yet)

## Slide 17: FGT cosmic ray - residual
Use the top and bottom quadrants to determine the projected value for the middle quadrant.
Assuming all quadrants have same resolution:
Single detector position resolution = Residual at middle quad/1.22 (from simple geometry)
180um residual @ Middle => 150um resolution at each detector
ϕ
Sigma = 240um
Sigma = 0.6mrad
=> 180um @ R=30cm
R

## Slide 18: FGT cosmic ray - efficiency
“Good event”: with clean one cluster in R&ϕ of two quadrants and calculate efficiency for third quadrant within good trigger area.
Sensitive to noise at higher HV & low Threshold.
 | Top | Middle | Bottom
3.3kV | 73% | 83% | 81% higher thr 76%
3.4kV | 83% | 88% | 78% higher thr 86%
3.5kV | 87% | 95% | 61% higher thr 86%
Top-Short “Golden event” Hit Map
Efficiency calculated in this area only
Middle-Long “Golden event” Hit Map
 | Top | Middle | Bottom
3.4kV | 72% | 60% | 70%
Efficiency calculated in whole octant
Dead HV sector 4
Default Thr= 4*PedRMS(~40)*3timebin ~ 500
Higher Thr = 7 * PedRMS(~40)*3timebin ~ 850
Use the cosmic ray results to decide which quadrant for final installation.
Reading the short octant

## Slide 19: FGT related measurements
The FGT will enhance the tracking capability of STAR in pseudorapidity range 1<η<2.
The primary FGT design is for W measurements in p+p collisions. But, together with other STAR detectors the following measurements may be possible.
  J/ψ e+e-, heavy flavor via electron decay channel.
  Charged hadron, i.g. π+π-.
  Drell-Yan?
  Jets?
Do we need larger GEM detectors?

## Slide 20: Forward Large Triple-GEM design at Temple University (I)
Supported by EIC R&D program.
The active area of Large Triple-GEM detectors is 10cm<R<100cm.
Each detector covers 30° azimuthal angle and use separate 2D readout.
12 GEM detectors are mounted on light-weight support structure
Schematics of the large GEM detector
GEM segmented side of the large GEM detector

## Slide 21: Forward Large Triple-GEM design at Temple University (II)
Lightweight (<1% X0 in active area)
Mylar foils plus spacer
Cathode (HV)
3 mm spacer (Drift volume)
3 x GEM foils + 2mm spacer grid
2mm spacer (Induction gap)
Readout electrode
spacer + Mylar foil
Gas, HV, and readout connections
16.45 mm thick
+ service box
Exploded view of the GEM detector
Large Triple GEM layout

## Slide 22: Forward Large Triple-GEM design at Temple University (III)
Study the mechanical deformation.
Study the gas diffusion inside the detector.
Cathode
GEM
GEM
GEM
Readout PCB
Low E field
High E field
Triple GEM
amplification
with diff HV conf.
Optimization of the signal size vs. electrode pitch

## Slide 23: Can GEM detectors be used for p+A collisions?
Question 1: Which measurements? For example, J/ψ production or di-hadron correlations to study gluon saturation in p+A.
Question 2: Will the higher multiplicity in p+A collisions (compare to p+p collisions) impact the resolution of GEM detectors?
Question 3: What kind of design of the GEM 2D readout board for p+A collisions? Strip only, strips plus pads, pad only or others?
All these questions should be answered by simulations first to study the feasibility.

## Slide 24: Summary
The STAR FGT has been fully installed for RHIC Run 13. Cosmic ray results provide the first stage calibration for the FGT.
Large Triple GEM detector R&D at Temple University is ongoing.
The application of GEM detector in p+A collisions need simulation studies.
Suggestions or comments on how to use GEM detectors in p+A collisions are very welcome!

## Slide 25: Thanks for your attention!
Thanks for the hard work of the STAR FGT group and Temple large GEM working group.
Special thanks
  Bernd Surrow, Maxence Vandenbroucke from Temple University,
  Akio Ogawa, Ramiro Debbe from BNL.
  Jason Bessuille, Ross Corliss, Gerrit van Nieuwenhuizen and Ben Buck from MIT.

## Slide 26: Backup
The FGT has 15 time bins.
One time-bin = 107nsec/4 = 27nsec
All strips with ADC sum 3 sigma above ped in a quadrant from 1 event are shown / panel
Timing moves 4 time-bin event by event due to cosmic system trigger only at RHIC clock